## Slide 1: SAP TechEd
Las Vegas, October 2–5
Demo Setup

## Slide 2: Szenarios
G-Suite (probably without SAP)
Mobile printing

## Slide 3: Hardware
Raspberry Pi 3B +
SD card + Micro USB power supply (2.5 A) +
Casing
Router
Able to print PDF
2x Lan cable
Wan connection
PLOSSYS 5

## Slide 4: IP Addresses
Dynamic IP address via DHCP
Creates internal subnet for - Raspberry Pi
- printer
Fixed IP address
Wan connection with external IP address
PLOSSYS 5: Public IP address

## Slide 5: Raspberry Pi
Connects to PLOSSYS 5
Announces the printer
Receives print jobs and forwards them to the printer
The software runs as a Docker container on the Pi
Must be configured with the printer‘s IP address
Web interface available to check the Docker container
Remote access via Ngrok should be possible
The SD card must be flashed with an image file (etcher.io)
  Download from delivery.sealsystems.de

## Slide 6: Restrictions
We can only print PDF
  No problem for G-Suite, since all documents are privided as PDF.
  Mobile printing: Other file formats WILL make trouble. (https://github.com/plossys/node-ipp-proxy/tree/master/packaging/linux/docker/kundentag2018#troubleshooting)
No print options

## Slide 7: Mobile Print
Possible via our „PLOSSYS DocPrint“ app (Android, iOS)
Must only set to the address of our PLOSSYS in the cloud.
Username and print options are ignored.

## Slide 8: To-Do List
Create shopping list (Michael)
Create G-Suite organization and account for Jon (Michael)
Deploy add-on (Michael)
Get the hardware (Jon)
Setup router (internal subnet for Raspberry Pi, printer, notebook) (Jon, Michael)
Upload image file for SD card (Michael)
Flash SD card (Jon)
Start PLOSSYS 5 in the cloud (Michael)
Setup mobile printing on a device (Jon, Michael)
Test (Jon, Michael)